## Slide 1
BIRLAMEDISOFT
We Care Health Care…
ELV
Extremely Low Voltage Systems
Presents

## Slide 2
www.birlamedisoft.com
Modules Covered
1. Structured Cabling for Data and Voice
2 . Access Control System
3. IP Video Surveillance System
4. Nurse Call System
5. Water Leaking Detection System
6. Fire Alarm System
7. Public Address System
8. Integrated Building Management System

## Slide 3
www.birlamedisoft.com
Structured Cabling for Data and Voice

## Slide 4
www.birlamedisoft.com
A Structured Cabling System is a cabling and connectivity products that integrates data, voice, video and various management system of a building
Introduction to Structured Cabling System

## Slide 5
www.birlamedisoft.com
Structured cabling is a system that can support the combined use of voice and data within the same network using the same network cable. This cabling system is designed to be installed using a "flood wiring" approach.
The use of "flood wiring" should ensure that all possible locations of premises, (subject to the customer’s requirements) that can be occupied by a user is covered by the structured data cabling. If planned correctly "flood wiring" should prevent any further data cabling from being necessary when adding new users or relocating existing ones.
Because of this systems flexibility to support voice and data at whatever location, structured cabling will not only future proof your premises
Structured Cabling System Description

## Slide 6
www.birlamedisoft.com
Redundancy at design stage reduces downtime & repair time
Concealed cabling
Ease of fault location & repair
Flexibility, expandability & modular connecting platform
Ease of moves, adds and changes
Enhanced end-use understanding and control
Continuous product support and warranty
Significant long term cost containment
Benefits of Structured Cabling System

## Slide 7
www.birlamedisoft.com
Access Control System

## Slide 8
www.birlamedisoft.com
Access Control Introduction
  Access control is the collection of mechanisms that permits managers of a system to exercise a directing or restraining influence over the behavior, use, and content of a system. It permits management to specify what users can do, which resources they can access, and what operations they can perform on a system.
The three main security principles pertaining to access control are:
  Availability
  Integrity
  Confidentiality
  Identification, Authentication, and Authorization are distinct functions.

## Slide 9
www.birlamedisoft.com
Identification
  Identification :
  Method of establishing the subject’s (user, program, process) identity.
    Use of user name or other public information.
    Know identification component requirements.

## Slide 10
www.birlamedisoft.com
Authentication
Authentication: Method of proving the identity.
    Something a person is, has, or does.
    Use of biometrics, passwords, passphrase, token, or other private information.
    Strong Authentication is important
    Biometrics : Verifies an identity by analyzing a unique person attribute or behavior (e.g., what a person “is”).
    Most expensive way to prove identity, also has difficulties with user acceptance.
    Many different types of biometric systems, know the most common.
    Most common biometric systems:
    Fingerprint
    Palm Scan
    Hand Geometry
    Iris Scan
    Signature Dynamics
    Keyboard Dynamics
    Voice Print
    Facial Scan
    Hand Topography
    Passwords : User name + password is the most common identification, authentication scheme.

## Slide 11
www.birlamedisoft.com
Authorization
  Authorization : Determines that the proven identity has some set of characteristics associated with it that gives it the right to access the requested resources.
Access Criteria can be thought of as:
  Roles
  Groups
  Location
  Time
  Transaction Types
Authorization concepts to keep in mind:
  Authorization Creep
  Default to Zero
  Need to Know Principle
  Access Control Lists
Problems in controlling access to assets:
  Different levels of users with different levels of access
  Resources may be classified differently
  Diverse identity data
  Corporate environments keep changing

## Slide 12
www.birlamedisoft.com
Access Control Models
Three Main Types:
  Discretionary : A system that uses discretionary access control allows the owner of the resource to specify which subjects can access which resources.
  Access control is at the discretion of the owner.
  Mandatory : Access control is based on a security labeling system. Users have security clearances and resources have security labels that contain data classifications.
  This model is used in environments where information classification and confidentiality is very important (e.g., the military).
  Non-Discretionary (Role Based) : Role Based Access Control (RBAC) uses a centrally administered set of controls to determine how subjects and objects interact. Is the best system for an organization that has high turnover.

## Slide 13
www.birlamedisoft.com
Access Control Techniques
There are a number of different access controls and technologies available to support the different models.
Rule Based Access Control
  Uses specific rules that indicate what can and cannot happen between a subject and an object.
  Not necessarily identity based.
  Traditionally, rule based access control has been used in MAC systems as an enforcement mechanism.
Constrained User Interfaces:
  Restrict user’s access abilities by not allowing them certain types of access, or the ability to request certain functions or information
Access Control Matrix:
  Is a table of subjects and objects indicating what actions individual subjects can take upon individual objects.
Content Dependent Access Control:
  Access to an object is determined by the content within the object.
Context Based Access Control:
Makes access decision based on the context of a collection of information rather than content within an object.

## Slide 14
www.birlamedisoft.com
Access Control Administration
First an organization must choose the access control model (DAC, MAC, RBAC).
Then the organization must select and implement different access control technologies.
Access Control Administration comes in two basic forms:
  Centralized : One entity is responsible for overseeing access to all corporate resources.
  Provides a consistent and uniform method of controlling access rights.
    Protocols: Agreed upon ways of communication
    Attribute Value Pairs: Defined fields that accept certain values.
    Decentralized :
  Gives control of access to the people who are closer to the resources
  Has no methods for consistent control, lacks proper consistency.

## Slide 15
  Physical Controls
  Network Segregation
  Perimeter Security
  Computer Controls
  Work Area Separation
  Data Backups
  Cabling
  Control Zone
  Technical (Logical) Controls
  System Access
  Network Architecture
  Network Access
  Encryption and protocols
  Auditing
www.birlamedisoft.com
Access Control Methods
Access controls can be implemented at various layers of an organization, network, and individual systems
Three broad categories:
  Administrative
  Physical
  Technical (aka Logical)
Administrative Controls
  Policy and Procedure
  Personnel Controls
    Separation of Duties
    Rotation of Duties
    Mandatory Vacation
  Supervisory Structure
  Security Awareness Training
  Testing

## Slide 16
www.birlamedisoft.com
Access Control Monitoring
Intrusion Detection
  Three Common Components
    Sensors
    Analyzers
    Administrator Interfaces
  Common Types
    Intrusion Detection
    Intrusion Prevention
    Honeypots
    Network Sniffers
Two Main Types of Intrusion Detection Systems
  Network Based (NIDS)
  Host Based (HIDS)
HIDS and NIDS can be:
  Signature Based
  Statistical Anomaly Based
    Protocol Anomaly Based
    Traffic Anomaly Based
  Rule Based

## Slide 17
www.birlamedisoft.com

## Slide 18
www.birlamedisoft.com
IP Video Surveillance

## Slide 19
www.birlamedisoft.com
IP Video Surveillance System Introduction
Closed-circuit television (CCTV) is the use of video cameras to transmit a signal to a specific, limited set of monitors. It differs from broadcast television in that the signal is not openly transmitted, though it may employ point wireless links. CCTV is often used for surveillance in areas, which need security, such as banks, casinos, airports etc. Modern CCTV cameras use small high definition color cameras that can not only focus to resolve minute detail, but by linking the control of the cameras to a computer, objects can be tracked automatically

## Slide 20
www.birlamedisoft.com
IP Video Surveillance Architecture

## Slide 21
www.birlamedisoft.com
Kinds of IP Cameras
An Internet protocol camera, or IP camera, is a type of digital video camera commonly employed for surveillance, and which unlike analog closed circuit television (CCTV) cameras can send and receive data via a computer network and the Internet. Although most cameras that do this are webcams, the term "IP camera" or "netcam" is usually applied only to those used for surveillance.
There are two kinds of IP cameras:
Centralized IP cameras, which require a central Network Video Recorder (NVR) to handle the recording, video and alarm management.
Decentralized IP cameras, which do not require a central Network Video Recorder (NVR), as the cameras have recording functionality built-in and can thus record directly to digital storage media, such as flash drives, hard disk drives or network attached storage.

## Slide 22
www.birlamedisoft.com
Working of IP Surveillance System

## Slide 23
www.birlamedisoft.com
Nurse Call System

## Slide 24
www.birlamedisoft.com
Features of Nurse Call System
Integrates with the best-selling digital telephone systems.
Text messaging for nurse call.
Unified, scalable architecture grows with your healthcare enterprise
Advanced technology provides high-quality communication.
Safe, low power operation does not interfere with medical equipment.
No monthly airtime or usage charges.

## Slide 25
www.birlamedisoft.com
Diagrammatic Representation of Nurse Call System

## Slide 26
www.birlamedisoft.com
Capabilities of Nurse Call System
Capabilities
  Immediate text display: patient, room info and call status
  Single button connects nurse to patient
  Auto-forwarding to alternate nurse
  Auto-delivery by shift from nurse master station

## Slide 27
www.birlamedisoft.com
Advantages of Nurse Call System
Patients
  Higher level of care and faster recovery
Nurses
  More time with patients, and better patient care
Physicians
  Direct access to nurses
Emergency department
  Faster response and increased efficiency
Specialties and support staff
  Coordinate efforts with other staff to improve productivity

## Slide 28
www.birlamedisoft.com
Water Leaking Detection System

## Slide 29
www.birlamedisoft.com
Introduction to Water Leak Detection System
Water Leak Detection System is used for integrated systems installed in "high-tech" buildings or those containing valuable artifacts, materials or other assets where early notification of a potentially damaging leak would be beneficial.
Leak detection systems must be unobtrusive, effective and robust enough to withstand getting dirty and the moderate physical abuse of other works being carried out under the same floor.
Zoned systems have a reputation for being safe, reliable and not prone to the same types of false alarms which those systems which use cumulative resistance techniques.

## Slide 30
www.birlamedisoft.com
Architecture of Water Leaking Detection System

## Slide 31
www.birlamedisoft.com
Working of Water Leaking Detection System
The water leak detector cable.
The cable itself is the sensor. Every centimetre of rugged, fire rated cable is sensitive to water and when water comes into contact with the cable, the system is able to detect the leak & report the location.
The detection cable can be installed in any length from a few metres in a drip tray to hundreds of metres around the perimeter of an office area. Typical applications in office buildings include the monitoring of fan-coil units around the edge of the building office floors, detectors surrounding the central utility core on each floor of the building and dedicated monitoring of leaks in electrical switch gear rooms, server rooms, network communications, etc. Each section of sensor cable is monitored by an inexpensive Sensor Interface Module. Various models are available with and without relay contacts and digital displays, but all modules are easily networked back to a central alarm panel or interfaced directly to the LAN as easy to design and install as a simple water leak detection system for one or two rooms or as a major installation in industrial complexes and high rise buildings.

## Slide 32
www.birlamedisoft.com
Diagram of Water Leaking Detection System

## Slide 33
www.birlamedisoft.com
Benefits of Water Leaking Detection System
• Improved operational efficiency.
• Lowered water system operational costs.
• Reduced potential for contamination.
• Extended life of facilities.
• Reduced potential property damage and water system liability.
• Reduced water outage events.
• Improved public relations.

## Slide 34
www.birlamedisoft.com
Fire Alarm System

## Slide 35
www.birlamedisoft.com
Fire Alarm System Introduction
An automatic fire alarm system is designed to detect the unwanted presence of fire by monitoring environmental changes associated with combustion. In general, a fire alarm system is classified as either automatically actuated, manually actuated, or both. Automatic fire alarm systems are intended to notify the building occupants to evacuate in the event of a fire or other emergency, report the event to an off-premises location in order to summon emergency services, and to prepare the structure and associated systems to control the spread of fire and smoke.

## Slide 36
www.birlamedisoft.com
Fire Alarm System Features
A key aspect of fire protection is to identify a developing fire emergency in a timely manner, and to alert the building's occupants and fire emergency organizations.
This is the role of fire detection and alarm systems. Depending on the anticipated fire scenario, building and use type, number and type of occupants and criticality of contents and mission, these systems can provide several main functions:
First, they provide a means to identify a developing fire through either manual or automatic methods.
Second, they alert building occupants to a fire condition and the need to evacuate.
Another common function is the transmission of an alarm notification signal to the fire department or other emergency response organization.
They may also shut down electrical, air handling equipment or special process operations, and they may be used to initiate automatic suppression systems.

## Slide 37
www.birlamedisoft.com
Fire Alarm System Configuration

## Slide 38
www.birlamedisoft.com
Architecture of Fire Alarm System

## Slide 39
www.birlamedisoft.com
Benefits of Fire Alarm System
The main advantage of installing fire alarms is the early warning benefit. The fire alarms can be installed just about any where in a commercial building and best of all the fire safety measure is highly cost effective for smoke and fire protection.
Early warning is essential to effective fire safety because fires can occur anytime and any place. We highly recommend having fire alarms installed on every floor of your commercial business because a fire can ignite even when people are not within a room or section of the building.
You can be immediately alerted of a fire at your commercial building when your fire alarm system is connected to a remote monitoring station. This early warning signal is extremely important to life safety for the following reasons:
Increases evacuation time for building occupants before a fire spreads out of control.
Emergency medical help can be immediately sent out to those in need.
Fire department personnel can help people exit the building safely.
  Easier to install.
  More system status information at the panel and central station.
  Input / Output programming much more flexible.
  Usually much more room available to expand.

## Slide 40
www.birlamedisoft.com
Public Address System

## Slide 41
www.birlamedisoft.com
Public Address System Introduction
A public address system (PA system) is an electronic sound amplification and distribution system with a microphone, amplifier and loudspeakers, used to allow a person to address a large public, for example for announcements of movements at large and noisy air and rail terminals.
The term is also used for systems which may additionally have a mixing console, and amplifiers and loudspeakers suitable for music as well as speech, used to reinforce a sound source, such as recorded music or a person giving a speech or distributing the sound throughout a venue or building.

## Slide 42
www.birlamedisoft.com
Components of a Public Address System
Sound sources: equipment that generates sound as an analogue, electrical or digital signal. Examples include microphones, CD players, electric guitars, synthesizers and samplers.
A mixing desk: a device with which to control, balance and treat the various sound sources. The mixer may have a series of inputs which allow most types of sound sources to be connected and routed to the next part of the signal chain.
Signal processors: devices used to treat or manipulate the signal from the sound sources so as to make it conform to the desired effect. Examples include compressors, reverb units and equalizers. Some of these may be in the mixing desk and some may be external devices.
Amplifiers: devices designed to increase the level of the mixed and treated signals to the point at which they can be transmitted to a loudspeaker to create sufficient volume.
Loudspeakers (or speakers): these convert the electrical signal from an amplifier into sound waves and direct the resultant sound into the auditorium.

## Slide 43
www.birlamedisoft.com
Working of Public Address System

## Slide 44
www.birlamedisoft.com
Configuration of Public Address System

## Slide 45
www.birlamedisoft.com
Architecture of Public Address System

## Slide 46
www.birlamedisoft.com
Benefits of Public Address System
Reduced and easy maintenance
Simple, reduced and economical field cabling
Trouble free system
Flexibility to connect the loudspeakers at longer distance.
Modular architecture
Flexibility to build the system for the present need with enough provision for future expansion.
Connectivity of P.A. system with the EPABX System
Monitoring the healthiness of all associated equipment in the PA System
Call attention chime tone prior to all announcements
Facility of connecting emergency siren over the paging channel
No use of AC Power source in the field
Highest priority for control desk paging
Bass and Treble control to custom-tailor the frequency response, for poor acoustic or highly noisy environments
LED Bar graph in dB scale to read the relative power
Distribution of audio signal through buffered O/P

## Slide 47
www.birlamedisoft.com
Integrated Building Management System

## Slide 48
www.birlamedisoft.com
Integrated Building Management System
All Buildings have some form of mechanical and electrical services in order to provide the facilities necessary for maintaining a comfortable working environment. These services have to be controlled by some means to ensure comfort conditions. Basic controls take the form of manual switching, time clocks or temperature switches. Here if Integrated Building Management System (BMS), is introduced, we are able to get a comfortable working environment in an efficient way.

## Slide 49
www.birlamedisoft.com
Features of Building Management System
Central controlling facility
Automate and take control of various operations
Manage and Coordinate the various systems
Provide a comfortable working environment in an efficient way.
Its purpose is to control, monitor and optimize building services
E.g., lighting; heating & cooling; security ; audio-visual and entertainment systems; ventilation and climate control; time & attendance control and reporting

## Slide 50
www.birlamedisoft.com
Modules integrated into Building Management System

## Slide 51
www.birlamedisoft.com
Architecture of Building Management System

## Slide 52
www.birlamedisoft.com
Building Management System - Connectivity

## Slide 53
www.birlamedisoft.com
Configuration of Building Management System

## Slide 54
www.birlamedisoft.com
Advantages of Building Management System
With the usage of various building automation techniques the energy efficiency is possible
With the help of occupancy sensors provided in various areas of the building, the service plants can be brought into operation only when needed and also to the optimum, thereby leading to huge energy savings
BMS improves quality of built environment, efficiency of workstations, while allowing great savings in energy consumption
Provide an acceptable level of temperature and humidity and safe guard against odours and indoor air pollutants.
Life safety factors involved in Intelligent Buildings are:
  Closed-circuit television
  Card access control
  Smoke detection
  Emergency control of elevator, doors ,HVAC system
  UPS
  ‘Data access’ security

## Slide 55: Corporate Office : Birlamedisoft Pvt. Ltd. 111 , 311 & 411, Gulmohar Centre Point, Pune Nagar Road, Near Vibhute Hospital, Opp. Kothari Wheels Maruti Showroom, Pune 411014, INDIA. Toll Free No: 1-800-3070-2090 Global Contact No. : +91 9021 156 156 Customer Support : Cell : +91-92256 22058, +91-92256 22059 , +91-92255 62180 Landline : +91-20-65106272 Email : support@birlamedisoft.com Sales Enquiry : Cell : +91-98232 90336, +91-94031 36401 / 402 / 403 , +91-9225061528 Landlines : +91-20-20261169, +91-20-20261171/72 , +91-20-65106271 / 72 / 73 Fax : +91-20-27036459 Email: info@birlamedisoft.com, birlamedisoft@gmail.com (General info / Sales) Skype : Birlamedisoft Website : www.birlamedisoft.com
www.birlamedisoft.com
Contact Us

## Slide 56
www.birlamedisoft.com
Thank You!